## Slide 1: 小麥網
A Business Networking Solution based on 小米 router
Studio 215

## Slide 2: WHY EAP?
EAP : Enterprise Access Point

## Slide 3: SOHO
Pre-share key
Setup easily

## Slide 4: SMB with SOHO AP
Pre-share key
Setup one by one
SMB : Small and Medium Business

## Slide 5: SMB with EAP
Enterprise Authentication
Setup by access controller
access controller
SMB : Small and Medium Business

## Slide 6: SMB with EAP
Network Management System
SMB : Small and Medium Business

## Slide 7: Applicable Environment
Coffee shop
Restaurant
Hotel
City hall
Stadium
Museum

## Slide 8: WHY US ?

## Slide 9: Mass and Prestige
Chart: Maximum Stations
| 小米路由器 mini | Aruba AP
Maximum stations | 20 | 100
Aruba : A networking vendor selling enterprise wireless LAN equipment

## Slide 10: Mass and Prestige
Chart: Price
| 小米 mini | 5 *小米mini | Aruba AP
Price | 650 | 3250 | 30000
Only needs 10% costs !!

## Slide 11: Mass and Prestige
Cheaper
Using Different Channel
Chart: 頻寬比較
| 小米mini (20 人) | 5*小米mini (100人） | Aruba AP （100人）
每人分到頻寬 (Mbps) | 43.335 | 43.335 | 8.667
802.11ac /256 QAM/160 MHz channel/ 400ns GI

## Slide 12: EAP Function Introduction

## Slide 13: Function feature
EAP Platform
(HW/FW)
Authentication/ Security/Firewall
Management SW
SON algorithm
Easy Configuration
Multiple SSIDs
Fast Roaming

## Slide 14: Function feature
EAP Platform
(HW/FW)
Authentication/ Security/Firewall
Management SW
SON algorithm
802.1X authentication
Radius server
Facebook Wi-Fi
Portal login interface
LDAP

## Slide 15: Function feature
EAP Platform
(HW/FW)
Authentication/ Security/Firewall
Management SW
SON algorithm
Dynamic Frequency Selection
Transmit Power Control
Auto Planning

## Slide 16: Function feature
EAP Platform
(HW/FW)
Authentication/ Security/Firewall
Management SW
SON algorithm
Network Management System

## Slide 17: EAP Platform

## Slide 18: Architecture
Raspberry Pi

## Slide 19: EAP Platform
Hardware – 小米路由 mini
Soc Vendor | MTK
CPU/Speed | MT7620A/580MHz
Non-volatile storage | 16M
RAM | 128M
Wireless Standard | 802.11a, 802.11b, 802.11g, 802.11n, 802.11ac
Frequency | 2.4GHz & 5GHz

## Slide 20: EAP Platform
Hardware – Raspberry pi
Soc Vendor | BroadCom
CPU/Speed | BCM2837/1.2GHz
Non-volatile storage | SD card(we use 16GB)
RAM | 1GB
Wireless Standard | 802.11n

## Slide 21: SSID by VLAN Tag
SSID=Enterprise
VLAN=1
------------------------------
50M/30M bps
SSID=Guest
VLAN=2
------------------------------
2M/1M bps
Multiple SSID for security management
Captive portal for authentication
Fast roaming
Traffic control

## Slide 22: Facebook Login & 802.1x
SSID=Enterprise
VLAN=1
------------------------------
50M/30M bps
SSID=Guest
VLAN=2
------------------------------
2M/1M bps
Radius server
802.1X
Facebook
wifidog

## Slide 23: Self-organization Network

## Slide 24: Why Self-organization Network?
High Density Development
Complicate Environment

## Slide 25: How?
Channel Scan
  Period scan
Simulate environment
  Construct path loss model

## Slide 26: SON feature
Channel Selection
Auto Planning
Transmit Power Control

## Slide 27: SON feature
Channel Selection
Auto Planning
Transmit Power Control

## Slide 28: Dynamic Channel Allocation

## Slide 29: SON feature
Channel Selection
Auto Planning
Transmit Power Control

## Slide 30: Transmit Power Control

## Slide 31: SON feature
Channel Selection
Auto Planning
Transmit Power Control

## Slide 32: Site Survey & Auto Planning
How many APs to satisfy full coverage.
With fixed number of APs, placement of them by satisfying the best coverage.

## Slide 33: Network Management System

## Slide 34: Easy Management & Centralized
Overview
Service 狀態

## Slide 35: Easy Management & Centralized
AP AC station table
AC list

## Slide 36: Easy Management & Centralized
AP AC station table
AP list

## Slide 37: Easy Management & Centralized
AP AC station table
station list

## Slide 38: Easy Management & Centralized
IP table setting

## Slide 39: Easy Management & Centralized
Auto Plan

## Slide 40: Future Works

## Slide 41: Future Works
Indoor Location Services
Mobile Alert

## Slide 42: Future Works
Indoor Location Services
Mobile Alert

## Slide 43: Why
personalized
push notifications
indoor map & directions
visiting route
asset tracking
For Store
For Enterprise

## Slide 44: Where
Customer
Orientation
Geo Fencing
Visiting Route

## Slide 45: How
ESP8266

## Slide 46: Prototype
Device
ESP8266
NMS
Sniffing The Packet of Device
&
Get The RSSI
Use The Algorithm
Send Packet

## Slide 47: Feature

## Slide 48: Future Works
Indoor Location Services
Mobile Alert

## Slide 49: Mobile alert
Server online/offline alert
Intrusion-detection alert
SON algorithm

## Slide 50: Thank you